Silicon: From Design to Production
Shankar Viswanathan
BLU - 2019/10/16

---
For starters ...
- This is meant as a very high-level introduction to the product development process
- I am not an expert on anything
- Ask questions at any time

---
Outline
- Design process
- Silicon manufacturing and test
- Volume production

---
Design Flow
Product
Definition
High-level model
simulation
Logic (RTL)
Design
RTL design
verification
Physical Design
Physical verification

---
Design Flow
Product
Definition
High-level model
simulation
Logic (RTL)
Design
RTL design
verification
Physical Design
Physical verification

---
Product Definition
- Technology node
- Features
- Power
- Performance
- Chip Area (== cost)
Image: amd.com

---
Example: AMD EPYC2
Image: https://www.servethehome.com/amd-epyc-7002-series-rome-delivers-a-knockout/4/

---
High-level design
- Design features broken down into smaller logic blocks
- Pipeline structure determined
Image: https://www.amd.com/en/technologies/zen-core

---
High-level Models
- Performance simulator
- Power estimation simulations
- Rough floorplan & chip area estimation

---
Design Flow
Product
Definition
High-level model
simulation
Logic (RTL)
Design
RTL design
verification
Physical Design
Physical verification

---
Logic Design
- Typically done using a Hardware Description Language such as Verilog
- Often uses libraries of commonly used elements like FIFOs, arrays, muxes
- Abstract behavioral models of analog elements – e.g. clock generator, high-speed IO drivers
- Needs to be aware of pipelines and timing

---
Verilog example: 4-input mux
sel[1:0]
module mux4(
    input [3:0] a,
    input [3:0] b,
    input [3:0] c,
    input [3:0] d,
    input [1:0] sel,
    output reg [3:0] out);
always @* begin
  case(sel[1:0])
    2’b00: out[3:0] = a[3:0];
    2’b01: out[3:0] = b[3:0];
    2’b10: out[3:0] = c[3:0];
    2’b11: out[3:0] = d[3:0];
  endcase
end
endmodule
a[3:0]
b[3:0]
out[3:0]
mux4
c[3:0]
d[3:0]

---
Another example
module lshift (input d,
        input clk,
        input rst_l,
        output reg [3:0] sreg);
   always @ (posedge clk) begin
      if (!rst_l) begin
        sreg[3:0] <= 4'b0;
      end else begin
        sreg[3:0] <= {sreg[2:0], d};
      end
   end
endmodule
- What does this do?
- How is it different from previous mux example?

---
Special Consideration: DFx
- Design For Test:
  - JTAG, Scan, Loopback modes
- Design For Debug:
  - Performance counters, HW breakpoints, Debug output pins

---
Design Verification
- Design verification is done to confirm that the design meets specification, i.e. is functionally correct
  - Cost of missed bugs can be very severe in terms of material cost and TTM
- Uses a mixture of simulation based checks as well as formal tools
- Unit-level as well as chip-level testbenches are constructed to run through different scenarios
  - Use both directed and constrained random tests to drive input
- Checkers and assertions are used to catch illegal conditions
- Extensive use of functional coverage and code coverage
- Generally 3 verification engineers for every RTL design engineer on the team

---
Testbench examples
Image: https://www.researchgate.net/figure/UVM-test-bench-Architecture-All-complex-test-benches-may-be-architected-as-shown-in-the_fig1_303759959
Image: https://verificationacademy.com/verification-horizons/june-2017-volume-13-issue-2/automation-and-reuse-in-risc-v-verification-flow

---
Simple Testbench: mux
module mux_tb_top;
  reg [3:0] a, b, c, d;
  wire [3:0] out;
  reg [1:0] sel;
  reg clk;
  integer i;
  mux4 mux4_i0(
    .a (a),
    .b (b),
    .c (c),
    .d (d),
    .sel (sel),
    .out (out));
initial begin
$dumpfile("dump.vcd");
$dumpvars(0, mux_tb_top);
sel[1:0] = 2'b0;
a[3:0] = $urandom;
b[3:0] = $urandom;
c[3:0] = $urandom;
d[3:0] = $urandom;
clk = 0;
i = 0;
  $monitor ("[%0t] sel=0x%0h a=0x%0h b=0x%0h c=0x%0h d=0x%0h out=0x%0h", $time, sel, a, b, c, d, out);
end
always #5 clk = ~clk;
always @ (posedge clk) begin
sel <= sel + 1;
c[3:0] <= $urandom;
d[3:0] <= $urandom;
i = i + 1;
end
always @(i) begin
if (i == 10)
$finish;
end
endmodule // mux_tb_top

---
Simulation Log
[0] sel=0x0 a=0x4 b=0x1 c=0x9 d=0x3 out=0x4
[5] sel=0x1 a=0x4 b=0x1 c=0xd d=0xd out=0x1
[15] sel=0x2 a=0x4 b=0x1 c=0x5 d=0x2 out=0x5
[25] sel=0x3 a=0x4 b=0x1 c=0x1 d=0xd out=0xd
[35] sel=0x0 a=0x4 b=0x1 c=0x6 d=0xd out=0x4
[45] sel=0x1 a=0x4 b=0x1 c=0xd d=0xc out=0x1
[55] sel=0x2 a=0x4 b=0x1 c=0x9 d=0x6 out=0x9
[65] sel=0x3 a=0x4 b=0x1 c=0x5 d=0xa out=0xa
[75] sel=0x0 a=0x4 b=0x1 c=0x5 d=0x7 out=0x4
[85] sel=0x1 a=0x4 b=0x1 c=0x2 d=0xf out=0x1
[95] sel=0x2 a=0x4 b=0x1 c=0x2 d=0xe out=0x2

---
Waveform view

---
Design Flow
Product
Definition
High-level model
simulation
Logic (RTL)
Design
RTL design
verification
Physical Design
Physical verification

---
Physical Design Flow
Synthesis Tool
Gate-level Netlist
Verilog RTL
Layout
(GDS-II)
Timing,
Place & Route

---
Logic Synthesis
- Converts RTL description into logic gates
- Modern tools first minimize the logic and then map it to library of gate elements
- Takes timing targets and other size or power constraints as inputs
- Result is a netlist file that is a text representation of a schematic

---
Synthesis example
4:1 mux constructed from NAND gates and inverters

---
Timing, Place & Route
- Takes each gate and places corresponding layout cell in the block
- Routes interconnect (wires) between cells based on connectivity and timing constraints
- Clock tree generation
- Optimize and iterate for most compact layout that satisfies all constraints

---
Example: NAND gate
C = ~(A & B);
Image: Electric User’s Manual

---
Layout example: 4:1 mux
Image credit: http://cmosedu.com/jbaker/courses/ee421L/f13/students/lopeztel/proj/proj.html

---
Fullchip layout: MOS 6502
Image: http://www.visual6502.org

---
Physical Verification
- Run timing simulations
- Check if final netlist matches original RTL intent (logical equivalence)
- Check equivalence of netlist to final layout (LVS)
- Ensure final layout meets design rules (DRC)

---
Tapeout
- Final verified GDSII mask released to fab for initial sample production
- Cake and ice cream celebration ensues

---
In parallel ...
- Microcode & firmware design and testing
- Software development: firmware, BIOS, compilers, drivers etc.
- Advanced use case testing using FPGAs or emulators
- Test pattern generation for chip testing

---
Fabrication
Images: https://www.wired.com/2010/10/inside-a-state-of-the-art-cleanroom/

---
Wafer testing
- Wafers are first tested for basic defects – bad die are marked
- Wafer is cut into individual dies and good dies are sent for packaging
- Packaged chip is tested again for packaging related defects

---
Automated testing
- ATE equipment allows testing of the chip in a highly controlled environment
- Uses pre-generated pattern of inputs and compares the output to the known “golden” output values
Teradyne UltraFLex Tester

---
Initial bringup & validation
- Initial samples are taken to special labs for exhaustive electrical and functional testing
- Chip is placed in a PCB along with other components
- FW and SW are loaded and booted up on the system
- Any issues found are analyzed and debugged
- Power and performance are characterized across different parts
- Major issues may necessitate design changes :-(

---
Power/Performance characterization
- Major benchmarks and special microbenchmarks are run and settings tuned to get maximum performance across workloads
- Power measurements are analyzed to get optimal point on frequency vs. voltage curve (perf/watt optimization)
- Clock and power gating heuristics are improved to get reduced power under idle or low stress workloads

---
Compliance testing
- Exhaustive checks to ensure adherence to industry (or de-facto) standards
  - USB, DDR, PCIe etc.
  - “Plugfest” held to connect various 3rd party devices
- ISA compatibility: AMD64, RISC-V, MIPS etc.

---
Debugging Silicon
- Chip is a blackbox – can only look at I/Os
  - Oscilloscopes and logic analyzers can help look at the external I/Os
- JTAG based hardware debuggers help on-chip debugging using DFD features built into the chip:
  - HW breakpoints allow stopping execution on certain events
  - Debug triggers and scan dumps help get better insight into internal state in the chip
- Looking at performance counters in the chip can help identify certain performance bottlenecks and lead to better software optimization

---
JTAG
- Daisy-chained devices can be individual chips on a PCB or modules within the same chip
- In test mode, functional mode clocks are stopped, TCK clock is fed and TMS is enabled.
- JTAG commands are sent via the TDI pin. Output is observed on the TDO pin
By Vindicator - Own work., CC BY 2.5, https://commons.wikimedia.org/w/index.php?curid=838166

---
Volume Production
- Automated high-volume testing setup to test EVERY chip prior to shipment
  - ATE testing at various temperature & humidity conditions
  - System-level test for longer software-based tests
- Chips are sorted and binned based on what passed vs failed
  - E.g. a chip that failed some test(s) at 3GHz but passed all tests at 2.8GHz would be binned as a 2.8GHz part
- Failures are analyzed for yield improvement
- Feedback provided to next-generation designs

---
Shipment
- Chips are packaged and boxed for retail sale
- Also put into trays or reels for automated pick-and-place machines for PCB assembly

---
More questions?